## Slide 1
MEG 315 — APPLIED THERMODYNAMICS
AD-HTC Integrated Biorefinery Dashboard
Otto Cycle • Rankine Cycle • Heat Integration • FastAPI • SQLite
Group 28 Department of Mechanical Engineering University of Lagos • February 2026

## Slide 2
PROJECT OVERVIEW
What we built
Interactive dashboard simulating the AD-HTC biorefinery system
Otto Cycle (biogas ICE) — T-s diagram with 4 state points
Rankine Steam Cycle — h-s Mollier diagram with pump, boiler, turbine, condenser
Heat integration analysis — CHP waste heat vs AD + HTC demand
12 real biomass feedstocks with published data (stored in SQLite)
FastAPI backend with 4 RESTful API endpoints
SQLite database for feedstock data and calculation history
Animated SVG process schematic with live calculated values

## Slide 3
THEORY: WHAT IS AD-HTC?
Background and motivation
Anaerobic Digestion (AD):
• Bacteria decompose organic matter
without oxygen
• Inputs: biomass (manure, food waste, etc.)
• Outputs: biogas (CH₄ + CO₂) + digestate
• Operates at 35–40°C (mesophilic)
Hydrothermal Carbonization (HTC):
• Wet biomass heated under pressure
(180–260°C, 10–40 bar)
• Converts digestate → hydrochar
• Hydrochar: solid biofuel ≈ lignite coal
Why integrate them?
1. AD biogas → fuel for gas engine (electricity)
2. Engine exhaust → waste heat recovered
3. Waste heat → steam for HTC reactor
4. HTC converts digestate → valuable hydrochar
5. Result: closed-loop biorefinery maximising
energy recovery from biomass

## Slide 4
AD-HTC FUEL-ENHANCED GAS POWER CYCLE
System schematic (Energhx, 2025)
[Place cycle_schematic.png in project folder to auto-embed] Biomass → Homogenizer → AD (moisture-rich) + HTC (moisture-lean) AD → Biogas → Combustion → Compressor/Turbine → Electricity HTC Steam Cycle: Boiler ↔ Reactor (closed loop) Exhaust → Waste Heat Recovery → Steam Generation
Source: Energhx Research Group, Faculty of Engineering, University of Lagos

## Slide 5
THEORY: THERMODYNAMIC CYCLES
Otto gas cycle and Rankine steam cycle
GAS POWER CYCLE (Otto / Brayton)
1→2: Isentropic compression
T₂ = T₁ × r^(γ−1)
2→3: Constant-volume combustion
Q_in = Cp × (T₃ − T₂)
3→4: Isentropic expansion (power)
T₄ = T₃ / r^(γ−1)
4→1: Heat rejection (exhaust)
W_net = W_turb − W_comp
HTC STEAM CYCLE (Rankine)
A→B: Pump — raises pressure
w_pump = vf × ΔP × 100
B→C: Boiler — waste heat → steam
Superheated at P = 60 bar
C→D: HTC reactor — steam heats
digestate for carbonization
D→A: Condenser — steam returns
to liquid, cycle repeats

## Slide 6
TECHNOLOGY STACK & ARCHITECTURE
Full-stack web application
Layer | Technology | Purpose
Backend | Python / FastAPI | RESTful API for cycle calculations
Database | SQLite | Feedstock storage + calculation history
Validation | Pydantic | Input/output data validation
Frontend | HTML / CSS / JavaScript | Interactive dashboard UI
Charts | Chart.js | T-s, h-s, energy, mass, heat charts
Styling | Tailwind CSS (CDN) | Responsive layout
Schematic | SVG (programmatic) | Animated process flow diagram
Fonts | Google Fonts (DM Sans/Mono) | Typography

## Slide 7
API ENDPOINTS
RESTful API — main.py (FastAPI)
Method | Endpoint | Description | Returns
GET | / | Serve dashboard HTML | HTMLResponse
GET | /api/feedstocks | All 12 feedstocks from SQLite | JSON array
POST | /api/analyze | Run full cycle analysis | JSON result + stores in DB
GET | /api/history | Past calculations | JSON array from DB
POST /api/analyze accepts: feedstock_key, feed_rate, T1, compression_ratio, T3, mass_flow_air, t_steam_C, p_cond, eta_turbine, eta_pump, htc_temp Returns: otto{}, rankine{}, mass_balance{}, heat{}, olr

## Slide 8
DATABASE SCHEMA
SQLite — database.py
Table | Column | Type | Description
feedstocks | id | INTEGER PK | Auto-increment
feedstocks | key / name | TEXT | Identifier & display name
feedstocks | ts, vs | REAL | Total / volatile solids fraction
feedstocks | biogas_yield, ch4 | REAL | m³/kg VS, methane fraction
feedstocks | htc_yield, htc_hhv | REAL | Hydrochar yield & HHV
calculations | id, timestamp | INT, TEXT | Record ID & ISO timestamp
calculations | feedstock, inputs | TEXT, JSON | Key & full input params
calculations | otto_results | JSON | All Otto cycle outputs
calculations | rankine_results | JSON | All Rankine cycle outputs
calculations | heat_balance | REAL | kW surplus/deficit

## Slide 9
FEEDSTOCK DATABASE
12 real biomass types stored in SQLite
Feedstock | TS% | VS% | Biogas (m³/kg VS) | CH₄% | HTC Yield
Cow Manure | 18 | 80 | 0.280 | 60 | 48%
Food Waste | 25 | 90 | 0.550 | 62 | 45%
Rice Husk | 90 | 80 | 0.250 | 52 | 58%
Microalgae | 10 | 85 | 0.450 | 65 | 40%
Wood Chips | 85 | 92 | 0.200 | 55 | 65%
Corn Stover | 88 | 85 | 0.338 | 55 | 55%
Sugarcane Bagasse | 50 | 90 | 0.310 | 54 | 52%
+ Sewage Sludge, Pig Manure, MSW, Cassava Peel, Palm EFB

## Slide 10
OTTO CYCLE RESULTS
T₁=298K, r=10, T₃=1200K, ṁ_air=50 kg/s (from API)
Point | Process | T (K) | s (kJ/kg·K)
1 | Intake | 298.0 | 1.000
2 | Compression | 748.5 | 1.000
3 | Combustion | 1200.0 | 1.542
4 | Exhaust | 477.7 | 1.542
W_comp = 452.8 W_turb = 829.2 W_net = 376.4 kJ/kg η = 72.6% Electrical Power = 18819 kW | Thermal Recovery = 4642 kW

## Slide 11
RANKINE CYCLE RESULTS
P=60 bar, T_steam=500°C, P_cond=0.06 bar (from API)
Point | Description | h (kJ/kg) | s (kJ/kg·K)
A | Pump Inlet (sat. liquid) | 359.9 | 1.1450
B | Pump Outlet | 367.4 | 1.1450
C | Turbine Inlet (500°C) | 3423.1 | 6.8826
D | Turbine Exit | 2570.5 | 7.3016
w_net = 845.1 kJ/kg η_rankine = 27.7%

## Slide 12
HEAT INTEGRATION
CHP waste heat vs AD + HTC thermal demand
CHP waste heat = ṁ_air × Cp × (T₄ − T₁) × 0.45 (45% recovery factor)
AD demand = (feed kg/s) × Cp_water × (37°C − ambient)
HTC demand = (digestate kg/s) × Cp × (T_HTC − 37°C)
Heat balance = CHP output − AD demand − HTC demand
SURPLUS → System is self-sufficient (no external heating) DEFICIT → External heating required
API test: Heat balance = +4555.89 kW (SURPLUS) for Cow Manure at 10 t/day

## Slide 13
MASS & ENERGY BALANCE
Cow Manure at 10 t/day (from API)
Output | Value | Unit
Volatile solids | 1440 | kg/day
Biogas volume | 403 | m³/day
Methane volume | 242 | m³/day
Biogas mass | 484 | kg/day
Dry digestate | 576 | kg/day
Hydrochar | 276 | kg/day

## Slide 14
LIVE DEMO
Screenshots from running dashboard
[Insert screenshot: Dashboard with KPI cards and sidebar]
[Insert screenshot: T-s diagram (Otto) and h-s Mollier (Rankine)]
[Insert screenshot: Energy & mass balance charts]
[Insert screenshot: Heat integration chart with surplus/deficit badge]
[Insert screenshot: Animated process schematic]
[Insert screenshot: FastAPI Swagger docs at /docs]

## Slide 15
HOW TO RUN
1. Install dependencies:
pip install -r requirements.txt
2. Start the server:
python main.py
3. Open in browser:
http://localhost:8000
4. API docs (auto-generated):
http://localhost:8000/docs
5. Or open ad-htc-biomass-v2.html directly
(standalone mode, no API)

## Slide 16
CONCLUSION
Full-stack AD-HTC biorefinery simulation
FastAPI backend with 4 RESTful endpoints
SQLite database — feedstock storage + calculation history
Otto cycle (biogas ICE) with T-s diagram — η = 72.6%
Rankine steam cycle with h-s Mollier diagram — η = 27.7%
Heat integration: CHP waste heat vs AD + HTC demand
12 biomass feedstocks with real published data
Animated process schematic with live values
Zero-installation option: standalone HTML also works
Group 28 • MEG 315 • University of Lagos • February 2026